## Slide 1
Z transform is a compact way to analyse discrete-time signals and systems.
What it does?
Z-transform is a powerful mathematical tool used to convert the difference equations into algebraic equations. To solve the difference equations which are in time domain, they are converted first into algebraic equations in z-domain using Z-transform, the algebraic equations are manipulated in z-domain and the result obtained is converted back into time domain using inverse Z-transform.
x[n] → X(z)
Time domain → z-domain
Z-TRANSFORM
Z-transform has two types:
unilateral(one-sided) and bilateral(two-sided). The unilateral Z-transform considers samples from zero to infinity and is mainly used for solving difference equations with initial conditions. The bilateral Z-transform considers samples from negative infinity to positive infinity and is used for general signal and system analysis, including the region of convergence.
Bilateral Z-transform: Used when the signal has nonzero values at both negative and positive time indices. {to +∞}.
Unilateral Z-transform: Used when analysing a signal from onward, especially when initial conditions are given.{n=0 to +∞}.

## Slide 2
02
Equations, ROC & Advantages of Z-transform.
Bilateral Z-transform is the main general definition; unilateral form is useful with initial conditions.
BILATERAL (TWO-SIDED)
X(z) = Σ x[n] z⁻ⁿ, n = −∞ To ∞
UNILATERAL (ONE-SIDED)
X⁺(z) = Σ x[n] z⁻ⁿ, n = 0 To ∞
ROC (Region of Convergence): values of z for which the defining infinite sum converges.
Common causal sequence:
x[n] = aⁿu[n] ⇒ X(z) = 1/(1 − az⁻¹) = z/(z − a)
ROC: |z| > |a|
Advantages of Z-transform:
• The Z-transform converts the difference equations of a discrete-time system into linear algebraic equations so that the analysis become easy and simple.
• convolution in time domain is converted into multiplication in z-domain.
x[n] * h[n] ↔ X(z)H(z)
•z-transform exists for most of the signals for which discrete-time Fourier transform (DTFT) does not exist.
Limitation:
• Frequency domain response cannot be achieved and cannot be plotted.

## Slide 3
03
Q.Find Z-transform d(n - 4).
We know that
∴
Hence,
ROC: Entire z-plane except at .
Q.Find Z-transform and ROC of
The given sequence is a causal infinite-duration sequence, i.e.,
because
∴
This is a geometric series of infinite length, and converges if
Hence,
ROC:

## Slide 4
04
Applications & real-world use
1. DIGITAL FILTERS
Analyse FIR/IIR filters, poles and zeros, and frequency response.
Example: Removing unwanted noise from audio or sensor signals.
2. CONTROL SYSTEMS
Analyse discrete controllers and system stability in digital control systems.
Example: Controlling motor speed in a robot.
3. DIFFERENCE EQUATIONS
Convert recursive input-output equations into algebraic equations that are easier to solve.
Example: Calculating the output of a discrete-time system.
4. SIGNAL PROCESSING
Represent and analyse sampled audio, vibration, biomedical, and communication signals.
Example: Processing digital audio signals.
5. SYSTEM DESIGN
Use poles, zeros, and the Region of Convergence (ROC) to analyse system stability and causality.
Example: Checking whether a system is stable and whether its Z-transform exists.

## Slide 5
05
Questions
1.Find the X(z) of: x[n] = d(n+3),
2. Find the X(z) and ROC of: x(n) =-a^nu(-n -1)
Answer:Z^3

## Slide 6
06
Solution of Q.2:
(b) The given signal is a non-causal infinite duration sequence, i.e.
because
This is a geometric series of infinite length and converges if
Hence
ROC:
X(z) = Σ x[n] z⁻ⁿ, n = −∞ To ∞